## Slide 1: Data Move

## Slide 2: Move Instructions
Format
  mov src, dest
  src and dest can only be one of the following
    Immediate
    Register
    Memory

## Slide 3: Move Instructions
Format
  The only possible combinations of the (src, dest) are
    (immediate, register)
    (memory, register) load
    (register, register)
    (immediate, memory) limited
    (register, memory) store
没有(memory,memory)

## Slide 4: Data Formats
Move data instruction
  mov (general)
  movb (move byte)
  movw (move word)(2-byte)
  movl (move double word)(4-byte)
  movq (move quad word)(8-byte)
    Immediate can only be represented as 32-bit signed sign extension to the destination
  movabsq (move absolute quad word)
  absq中immediate会以64位的形式体现
Only update the specific register byte
  except movl which updates the higher-order 4 bytes of the register to 0(movl只能移动四字节，会将高位4bytes直接变为全0)

## Slide 5: Data Movement Example
movl $0x4050, %eax immediate register, 4 bytes
movw %bp, %sp register register, 2 bytes
movb (%rdi, %rcx), %al memory register, 1 byte
movb $-17, (%rsp) immediate memory, 1 byte
movq %rax, -12(%rbp) register memory, 8 byte
地址都应该是64位

## Slide 6: Move with Zero Extension
Move data instruction
  movz (move with zero extension)
  movzbw (move zero-extension byte to word)
  movzbl (move zero-extension byte to double word)
  movzbq (move zero-extension byte to quad word)
  movzwl (move zero-extension word to double word)
  movzwq (move zero-extension word to quad word)
  no movzlq, it is implemented by movl

## Slide 7: Move with Sign Extension
Move data instruction
  movs (move with sign extension)
  movsbw (move sign-extension byte to word)
  movsbl (move sign-extension byte to double word)
  movsbq (move sign-extension byte to quad word)
  movswl (move sign-extension word to double word)
  movswq (move sign-extension word to quad word)
  movslq (move sign-extension double word to quad word)

## Slide 8: Example
long exchange(long *xp, long y)
{
long x = *xp ;
*xp = y ;
return x ;
}
xp in %rdi, y in %rsi
exchange:
movq (%rdi), %rax Get x at xp. Set as return value
movq %rsi, (%rdi) Store y at xp
ret return
此处(%rdi)指的是指针xp指向的地址内的具体内容，%rdi是xp指向的地址

## Slide 9: Array in Assembly
Persistent usage
long a[16];
void f(void){
long i ;
for(i=0; i<16; i++)
a[i]=i;
}
movq %rdx, a(,%rdx,8(一个格一个byte，long 8个byte))
i:%rdx(但是此处并未声明i真正的具体地址)

## Slide 10: Data Movement Example
Initial value %dl=8d %rax =0000000098765432
movb %dl, %al %rax=000000009876548d
movsbl %dl, %eax %rax=00000000ffffff8d
movzbq %dl, %rax %rax=0000000000008d

## Slide 11: Stack operation
There are two stack operation instructions
  Push and Pop
Push
  decreases the %rsp (enlarge the stack)
  (栈顶在地址小的一端，push应该减去元素长度)
  stores the value in a register into the stack
Pop
  stores the value in the top of the stack into a register
  increases the %rsp (shrink the stack)

## Slide 12: Stack operations
%rax | 0x123
%rdx | 0
%rsp | 0x108
pushq %rax
Stack “top”
0x108
%rsp

## Slide 13: Stack operations
%rax | 0x123
%rdx | 0
%rsp | 0x100
pushq %rax
0x100
Stack “top”
0x108
%rsp
pushq S
  R[%rsp]  R[%rsp]-8

## Slide 14: Stack(是memory的一部分) operations
%rax | 0x123
%rdx | 0
%rsp | 0x100
pushq %rax
0x100
Stack “top”
0x123
0x108
%rsp
pushq S
  1.R[%rsp]  R[%rsp]-8(先向下减去内容长度)
  2.M[R[%rsp]]  S(再将元素置入对应位置)
Push quad word

## Slide 15: Stack operations
%rax | 0x123
%rdx | 0
%rsp | 0x100
popq %rdx
0x100
Stack “top”
0x123
0x108
%rsp

## Slide 16: Stack operations
popl D
  D  M[R[%rsp]]
%rax | 0x123
%rdx | 0x123
%rsp | 0x100
popq %rdx(pop出来的内容置入register)
0x100
Stack “top”
0x123
0x108
%rsp

## Slide 17: Stack operations
popl D
  D  M[R[%rsp]]
  R[%rsp]  R[%rsp]+8
Pop quad word
%rax | 0x123
%rdx | 0x123
%rsp | 0x108
popq %rdx
0x100
Stack “top”
0x123
0x108
%rsp

## Slide 18: Example
int main()
{
long a = 4 , b = 3, c = 2;
decode1(&a, &b, &c); (此时的参数只能置入memory因为我们需要的是地址中的内容)
printf(“a = %d, b = %d, c = %d\n”, a, b, c);
}

## Slide 19: Example
2
Stack
•
•
•
3
4
a
b
Can the variable either a or b or c
be in a register? 不能
c
%rsp

## Slide 20: Example
void decode1(long *xp, long *yp, long *zp)
{
long x, y, z;
x = *xp ;
y = *yp;
z = *zp ;
*yp = x ;
*zp = y ;
*xp = z ;
}
movq (%rdi), %r8
movq (%rsi), %rcx
movq (%rdx), %rax
movq %r8, (%rsi)
movq %rcx, (%rdx)
movq %rax, (%rdi)
ret

## Slide 21: Example
movq (%rdi), %r8
movq (%rsi), %rcx
movq (%rdx), %rax
movq %r8, (%rsi)
movq %rcx, (%rdx)
movq %rax, (%rdi)
ret
2
Rtn adr
%rsp
Stack
•
•
•
3
4
a
b
c
%r8 | 4
%rcx | 3
%rax | 2

## Slide 22: Example
movq (%rdi), %r8
movq (%rsi), %rcx
movq (%rdx), %rax
movq %r8, (%rsi)
movq %rcx, (%rdx)
movq %rax, (%rdi)
ret
2
Rtn adr
%rsp
Stack
•
•
•
4
4
a
b
c
%r8 | 4
%rcx | 3
%rax | 2

## Slide 23: Example
movq (%rdi), %r8
movq (%rsi), %rcx
movq (%rdx), %rax
movq %r8, (%rsi)
movq %rcx, (%rdx)
movq %rax, (%rdi)
ret
3
Rtn adr
%rsp
Stack
•
•
•
4
4
a
b
c
%r8 | 4
%rcx | 3
%rax | 2

## Slide 24: Example
movq (%rdi), %r8
movq (%rsi), %rcx
movq (%rdx), %rax
movq %r8, (%rsi)
movq %rcx, (%rdx)
movq %rax, (%rdi)
ret
3
Rtn adr
%rsp
Stack
•
•
•
4
2
a
b
c
%r8 | 4
%rcx | 3
%rax | 2

## Slide 25: Example
a
b
c
movq (%rdi), %r8
movq (%rsi), %rcx
movq (%rdx), %rax
movq %r8, (%rsi)
movq %rcx, (%rdx)
movq %rax, (%rdi)
ret
3
%rsp
Stack
•
•
•
4
2
%r8 | 4
%rcx | 3
%rax | 2