## Slide 1: End-to-end Layer & DNS
IPADS, Shanghai Jiao Tong University
https://www.sjtu.edu.cn
SE124 (2021 Fall)
xx

## Slide 2: Review: Assurance of End-to-end Protocol
Assurance of at-least-once delivery
Assurance of at-most-once delivery
Assurance of data integrity
Assurance of stream order & closing of connections
Assurance of jitter control
Assurance of authenticity and privacy
Assurance of end-to-end performance

## Slide 3: 1. Assurance of At-least-once Delivery
RTT (Round-trip time)
  to_time + process_time + back_time (ack)
At least once on best effort network
  Send packet with nonce
  Sender keeps a copy of the packet
  Resend if timeout before receiving acknowledge
  Receiver acknowledges a packet with its nonce
Try limit times before returning error to app

## Slide 4: Review: Calculating RTT and Timeout (in TCP)
Exponentially Weighted Moving Average
  Estimate both the average rtt_avg and the deviation rtt_dev
  Procedure calc_rtt(rtt_sample)
    rtt_avg = a*rtt_sample + (1-a)*rtt_avg; /* a = 1/8 */
    dev = absolute(rtt_sample – rtt_avg);
    rtt_dev = b*dev + (1-b)*rtt_dev; /* b = 1/4 */
  Procedure calc_timeout(rtt_avg, rtt_dev)
    Timeout = rtt_avg + 4*rtt_dev

## Slide 5: How to Decide Timeout?
Fixed timer: dilemma of fixed timer
  Too short: unnecessary resend
  Too long: take long time to discover lost packets
Adaptive timer
  E.g., adjust by currently observed RTT, set timer to 150%
  Exponential back-off: doubling from a small timer
NAK (Negative AcKnowledgment)
  Receiver sends a message that lists missing items
  Receiver can count arriving segments rather than timer
  Sender can have no timer (only once per stream)
若receiver采用的是NAK来收包，那么就说明receiver是不使用timer的，即是不回去计算是否timeout的，只会去看到底接收到了哪些包(counting)，并且会 返回丢失包的列表

## Slide 6: 2. Assurance of At-most-once Delivery
At-least-once delivery
  Remember state at the sending side
  Tends to generate duplicated requests(幂等，receiver维护请求的tid)
At-most-once delivery
  Maintains a table of nonce at the receiving side
  The table may grow indefinitely
    Space and search time(trade-off between size and search-time)
    Tombstones (something that cannot be deleted forever)
  Another way: Make the application tolerate duplicated requests
    Recall the NFS collapse case: server wastes time to execute duplicated requests

## Slide 7: Duplicate Suppression
Monotonically increasing sequence number
  Receiver discards smaller nonce, only holds the last nonce, one per sender
  Now, the old nonce is a tombstone!
Use a different port for each new request
  Should never reuse the old port number
  But, the old port is now tombstone!

## Slide 8: Duplicate Suppression
Accept the possibility of making a mistake
  E.g., if sender always gives up after five RTT (cannot ensure at-least-once), then receiver can safely discard nonces that are older than five RTT(这种方式的问题:若一个packet正好对应于马上要被舍弃的那五个nonce中的第1个，(但是根据这种方式根本不应该被舍弃)，但是他却过了很长时间没有被接受，并且已经有新的包被接受了，那么这个包对应的nonce就会被舍弃使得这个慢的包在到达之后也不会被接受。)
  It is possible that a packet finally shows up after long delay (solution: wait long time)
Receiver crashes and restarts: lose the table
  One solution is to use a new port number each time the system restarts
  Another is to ignore all packets until the number of RTT has passed since restarting, if sender tries limit times
Anyway, duplicate suppression makes the system complex

## Slide 9: 3. Assurance of Data Integrity
Data integrity(数据完整性)
  Receiver gets the same contents as sender
Reliable delivery protocol
  Sender: adds checksum to the end-to-end layer
  Receiver: recalculates the checksum, discards if not match
Q: Is it redundant since link layer provides checksum?
  No. Besides network, there could be other errors, e.g., in memory copying
The assurance is not absolute
  What if a packet is mis-delivered and the receiver ACK?
1.link layer层面的checksum不多余，因为可能发生一些硬件层面的错误，如课件提到的memory copying，网卡问题等。
2.e2e层的checksum不是一定生效的，因为对于一些只进行计算的请求，他们的checksum可能是一样的，另外，也可能出现发错IP的情况，即一个错误的checksum发送到错误的IP addr也可能被接受。
hack：发送请求的时候，目标的IP一定要正确并且存在，但是sender的IP可以是错误的。

## Slide 10: 4. Segments and Reassembly of Long Messages
Bridge the difference between message and MTU
  Message length: determined by application
  MTU(max transfer utility): determined by network
Segment contains ID for where it fits
  E.g., "message 914, segment 3 of 7"
  Can be used for at-least-once and at-most-once delivery
Reassembly
  Out-of-order, mingled with other message's segments
  Allocating a buffer large enough to hold the message
由于将每个packet进行碎片化处理，锁需要等到每一个segment都被接受到的时候才能认为接收成功，所以需要一个较大的buffer来维护已经收到的segment的信息。

## Slide 11: When Out of Order…
Solution-1: Receiver only ACK in order packets, discards others(会丢弃明明已经收到的包)
  Waste of bandwidth(e.g.:接受到了1,2,3,4,这时候接收到6会被舍弃。)
Solution-2: ACK every packet and hold early packets in buffer, release the buffer when all in order
  Need using large buffer when waiting for a bad packet
Solution-3: Combine the two above
  Discard if buffer is full
  New problem: how much buffer?
Speedup for common case
  NAK to avoid timeout
  If NAKs are causing duplicates, stop NAKs
TCP is based on ACK, not NAK

## Slide 12: Closing of Connections
Open a stream
  Create a record to keep track of which elements have been sent, received, acknowledged
Close a stream
  When finish, it needs to report an end-of-stream
  Both ends need to agree last element is OK and then close
  1. Alice sends close request to Bob with stream record ID
  2. Bob checks and agrees, sends a close ACK
  3. Alice receives ACK, turn off sender, discard record
  4. Alice sends "all done" to Bob
  5. Bob receives "all done" and discard stream record
<- What if duplicate?

## Slide 13: 5. Assurance of Jitter Control
Real-time
  When reliability is less important than timely delivery
  A few error in a movie may not be noticed
  Jitter: variability in delivery time
Strategy
  Basic: delay all arriving segments

## Slide 14: 5. Assurance of Jitter Control
Measure the distribution of delays in a chart showing delay time vs. frequency of that delay
Choose an acceptable frequency of delivery failure
Determine Dlong that longer than 99% delay
Determine the shortest delay, Dshort
Calculate number of segment buffer:
  Dheadway is average delay between arriving segments
segement个数=
最晚到达的包的时间与最早到达的包的时间间隔除以平均的传输时间(即取计算在这个最长时间内会有多少包被传输并被接受)

## Slide 15: 6. Assurance of Authenticity and Privacy
Internet is dangerous
  Hostile intercepts and maliciously modifies packets
  Violate a protocol with malicious intent
Key-based mathematical transformations to data
  Sign and verify: establish the authenticity of the source and integrity of contents
  Encrypt and decrypt: maintain privacy of contents
Consideration
  False sense of security, worse than no assurance
加密只会使得内容不可见，但是并不能保证内容没有被改变，即attacker可以通过用修改过的加密内容修改原始加密内容来攻击，需要通过公钥和私钥来解决。

## Slide 16: 6. Security: Asymmetric Encryption(非对称加密)
Public Key VS. Private Key
  Public key: encrypt to identify reader (only me can read this)
  Private key: encrypt to identify writer (yes, it's me who wrote this)
  Poor performance, so just used to exchange symmetric key
Questions
  What is a certificate? Why using a CA (Certificate Authority)?
  How to exchange a symmetric key in HTTPS or SSH?
  What is the root of trust?
  Will be addressed later, in Security part

## Slide 17: 7. End-to-end Performance
Multi-segment message questions
  Trade-off between complexity and performance
  Lock-step protocol

## Slide 18: Overlapping Transmissions
Pipelining technique

## Slide 19: Overlapping Transmissions
Packets or ACK may be lost
  Sender holds a list of segments sent, check it off when receives ACK
  Set a timer (according to RTT) for last segment
If list of missing ACK is empty, OK
If timer expires, resend packets and another timer

## Slide 20: Fixed Window(固定窗口)
Receiver tells the sender a window size
Sender sends window
Receiver acks each packet as before
Window advances when all packets in previous window are acked
  E.g., packets 4-6 sent, after 1-3 ack'd
If a packet times out -> resend packets
Still much idle time
由于窗口是固定的，即一个窗口中的segment是确定的，所以此时的空白间隔时间(即receiver无事情可以做)为下一个窗口的第一个包到达的时间减去当前窗口中最后一个包的ACK被发送出去的时间。

## Slide 21: Sliding Window(滑动窗口,船口长度固定,但是内容动态变化)
Sender advances the window by 1 for each in-sequence ACK it receives
  Reduces idle periods
  Pipelining idea
But what's the correct value for the window?
  We'll revisit this question
  First, we need to understand windows
这张图片前提显然是网络是稳定的，但是实际上，可可能存在包4已经被接受，但是包3的ACK还未被接收的情况。

## Slide 22: Handling Packet Loss
流程:d1对应的a1倍sender接受之后，window后移，范围变成2-6，之后2发生了丢包，3-6正常，这时候即使sender接受到了a3，但是由于没有顺序的接收到a2，所以不能继续移动窗口，所以等在那里。等到sender已经接受到a6了还是没有接受到a2，认为发生了timeout，进行包2的resend。由于a6已经被接受，所以直接就变成了7-11

## Slide 23: Chose the Right Window Size
If window is too small
  Long idle time
  (考虑极端情况即可,若长度为1,只能顺序发送)
  Underutilized network
If window too large
  Congestion(堵塞，冲突)
  若window过大，那么可能出现的情况是
  sender在一段时间内可以连续发送大量的包，
  从而使得网络拥堵

## Slide 24: Sliding Window Size
window size ≥ round-trip time × bottleneck data rate
Sliding window with one segment in size
  Data rate is window size / RTT
Enlarge window size to bottleneck data rate
  Data rate is window size / RTT
Enlarge window size further
  Data rate is still bottleneck
  Larger window makes no sense
- Receive 500 KBps
- Sender 1 MBps
- RTT 70ms
- A segment carries 0.5 KB
- Sliding window size = 35KB (70 packets)
bottleNeck即是sender与receiver传输速率中的较小者,RTT指的是一个包被传输,处理到接收到ACK的时间度量,因而两者相乘实际上就是在计算在一个RTT内会被传输的最大数据量,因而如果window-size正好等于这个值,那么就会正好在任意时刻会”填满”传输网络而不会发生阻塞。
下面公式乘积结果就是第一个byte对应的ACK被接受的时候sender正好发出的byte的编号。

## Slide 25: Self-pacing: Sliding Window Size
Although the sender doesn't know the bottleneck, it is sending at exactly that rate
Once sender fills a sliding window, cannot send next data until receive ACK of the oldest data in the window
The receiver cannot generate ACK faster than the network can deliver data elements
RTT estimation still needed

## Slide 26
TCP and Congestion Control

## Slide 27: Congestion
Definition: Too many packets present in (a part of) the network causes packet delay and loss that degrades performance
Network & End-to-end layers share the responsibility for handling congestion
1. Network layer
  Directly experiences the congestion
  Ultimately determine what to do with the excess packets
2. End-to-end layer
  Control to reduce the sending rate,(比如调整slide-window-size) is the most effective way
network架构中网络包的接收顺序是从下到上的，因而network layer会先于end to end layer检测到congestion。

## Slide 28: Network Congestion

## Slide 29: Why Congest?
If all of a sudden, streams of packets begin arriving on three or four input lines and all need the same output line, a queue will build up
If there is insufficient memory to hold all of them, packets will be lost
Adding more memory may help up to a point, but
  Nagle (1987) realized that if routers have an infinite amount of memory, congestion gets worse, not better
  This is because by the time packets get to the front of the queue, they have already timed out (repeatedly) and duplicates have been sent
memory不够-->增加memory,但是这样做往往会加剧congestion,因为更多的memory就可以支持更长的queue,后到来的packet需要的等待时间就会更长,而TCP是基于ACK的，因而sender就更容易检测到超时从而进行重新发送，这就会导致同一个包会多次pending在同一个queue中，这只会使得congestion更加严重。

## Slide 30: Load Shedding: Setting Window Size
For performance:
  window size ≥ round-trip time × bottleneck data rate
For congestion control:
  window size ≤ min(RTT x bottleneck data rate, Receiver buffer)
  Congestion window
2 windows become 1
  to achieve best performance and avoid congestion

## Slide 31: Congestion Control
Basic idea:
  Increase congestion window slowly
  If no drops -> no congestion yet
  If a drop occurs -> decrease congestion window quickly
Use the idea in a distributed protocol that achieves:
  Efficiency: i.e., uses the bottleneck capacity efficiently
  Fairness, i.e., senders sharing a bottleneck get equal throughput (if they have demands)

## Slide 32: AIMD (Additive Increase, Multiplicative Decrease)
Every RTT:
  No drop: cwnd = cwnd + 1(线性增加)
  A drop: cwnd = cwnd / 2(指数下降)

## Slide 33: Problems with AIMD
Increases very slowly at the beginning
Initial window size is 1
  Probably too small in practice
Solution: do multiplicative increase at the beginning
  Congestion_window init = 1
  Initially, do Congestion_window ← 2 * Congestion_window each RTT until we hit congestion
  Named "slow start" (even though it's exponentially fast!)

## Slide 34: TCP Slow Start
At the beginning of the connection, exponential increase the window
  Double it every RTT until you see loss
  Decreases the time it takes for the initial window to "ramp up"
  So the name is really weird... it should be "fast start"

## Slide 35: TCP Fast Retransmit / Fast Recovery
When a sender receives an ACK with sequence number X, and then three(5-1(自己的那个)-1(丢包的那个)) duplicates of that packet, it immediately retransmits packet X+1
  Example: sender receives 5 6 6 6 6
  Infers that packet 7 is lost, immediately retransmits
  On fast-retransmit, window decrease is as before: W = W/2

## Slide 36: TCP Fast Retransmit / Fast Recovery
When a packet is lost due to timeout, (这时候会直接变成1重新开始)TCP behaves differently:
  W = 1, then do slow-start until the last good window
  Reasoning: if there is a retransmission due to timeout, then there is significant loss in the network, and senders should back way off

## Slide 37: Retrofitting TCP

## Slide 38: Retrofitting TCP
1. Slow start: one packet at first, then double until
  Sender reaches the window size suggested by the receiver
  All the available data has been dispatched
  Sender detects that a packet it sent has been discarded
2. Duplicate ACK
  When receiver gets an out-of-order packet, it sends back a duplicate of latest ACK
3. Equilibrium
  Additive increase & multiplicative decrease
4. Restart, after waiting a short time

## Slide 39: Fairness between Links

## Slide 40: AIMD Leads to Efficiency and Fairness
AI：只改变截距而不改变斜率，
所以是沿着x+y=C的垂直方向移动，所以是沿着平行于fairness线移动；
MD:每次截距变为原来的一半，所以与x,y同时除以2之后的点在同一条与原点之间的连线上面

## Slide 41: Q: Why not Additive Decrease
It does not converge to fairness
  from a congested point, (x',y'), reducing each by 1 worsens fairness and takes us away from the "ideal" outcome(只做加减法的话(x,y)一直会在某一条与x+y=C垂直的线上面移动，并且假设y>x的话，那么随着减小与原点的连线斜率会越来越大，也就是”take us away”,同时，之后还会进行additive increase，还会沿着原来的路径走回去，随意如果初始状态是unfair的，那么终止状态还是unfair的。同时做相同的加减法不会改变大小关系)

## Slide 42: Weakness of TCP
If routers have too much buffering, causes long delays
Packet loss is not always caused by congestion(还可能是网络本身问题)
  Consider wireless network: if losing packet, sender may send faster instead
TCP does not perform well in datacenters
  High bandwidth, low delay situations
TCP has a bias against long RTTs
  Throughput inversely proportionally to RTT
  Consider when sending packets really far away vs really close
Assumes cooperating sources, which is not always a good assumption

## Slide 43: Summary of Congestion Window
Reliability Using Sliding Window
  Tx Rate = W / RTT
Congestion Control
  W = min(Receiver_buffer, cwnd)
  Congestion window is adapted by the congestion control protocol to ensure efficiency and fairness
  TCP congestion control uses AIMD which provides fairness and efficiency in a distributed way

## Slide 44
The Design of DNS
Domain Name Service

## Slide 45: DNS: Binding IP and Domain Name
Names: hostname strings
  E.g., www.sjtu.edu.cn
Values: IP addresses
  E.g., 202.120.2.119
Look-up algorithm
  Resolves a hostname to an IP address so that your machine knows where to send packets

## Slide 46: IP Address as a Type of Name
An IP address itself is a type of name
  A structured name that is used to locate an object
  Use IP address to identify the server
    Recall your labs in ICS on socket
  On Internet
    The router will know where to send a packet with destination IP
Hostname has no such semantic
  A router does not know how to send a packet to "baidu.com"

## Slide 47: Why Not Just Using IP Address?
IPs are structured in a particular way for routing
  You cannot chose your IP address as you wish
    Note: usually an address cannot be picked
  While you can chose your host names
IPs are not user-friendly enough

## Slide 48: Questions on DNS
Q: Can a name have multiple values (IP addresses)?
  Yes
  This allows a web server to balance its load over multiple machines
  Also allows a client to choice a nearest IP to access
Q: Can a single value have multiple names?
  Yes
  This allows server consolidation

## Slide 49: Questions on DNS
Q: Can the value corresponding to a name change?
  Yes
  This allows to change the physical machine (with different IP) that stores the data without changing the hostname
  Such changing is hidden to clients

## Slide 50: Look-up Algorithm
At first, each machine kept a "hosts.txt" for address binding
  E.g., "r900 202.120.224.83"
  Using table look-up to resolve the binding
  This method cannot scale in Internet
1984, four Berkeley students wrote BIND
  Berkeley Internet Name Domain
  Still the dominant DNS software in use

## Slide 51: Distributing Responsibility
The binding
  Too large to be stored on a single machine
  Thus, the data are stored on many machines
    As known as "name servers"
How to know which name server has a particular binding?
  Solution: structure the hostname
  Names have a hierarchy, e.g., com, net, gov, correspond to "zones"
  Zones are mapped to name servers

## Slide 52: Name Servers
The root zone
  Maintained by ICANN, non-profit
The ".com" zone
  Maintained by VeriSign, add for money
The ".sjtu.edu.cn" zone
  Maintained by SJTU

## Slide 53: DNS Hierarchy (a partial view)

## Slide 54: Basic DNS Look-up Algorithm
Example: lookup IP of "ipads.se.sjtu.edu.cn"
Traverse the name hierarchy from the root
  The root will tell us the "cn" name server IP,
  which will tell us the "edu.cn" name server IP,
  which will tell us the "sjtu.edu.cn" name server IP,
  which will tell us the "se.sjtu.edu.cn" name server IP,
  which finally tells us the "ipads.se.sjtu.edu.cn" IP
Such algorithm is called delegation

## Slide 55: DNS Lookup

## Slide 56: DNS Lookup

## Slide 57: DNS Lookup

## Slide 58: DNS Lookup

## Slide 59: DNS Lookup

## Slide 60: Context in DNS
Names in DNS are global (context-free)
  A hostname means the same thing everywhere in DNS
Actually, it should be "ipads.se.sjtu.edu.cn."
  A hostname is a list of domain names concatenated with dots
  The root domain is unnamed, i.e., "." + blank

## Slide 61: Fault Tolerant
Each zone can have multiple name servers
  A delegation usually contains a list of name servers
  If one name server is down, others can be used

## Slide 62: Three Enhancements on Look-up Algorithm
1. The initial DNS request can go to any name server, not just the root server
  Even on your own machine: /etc/hosts
  You can specific name servers in /etc/resolv.conf
  If no record, just return address of the root server
  Q: what are the benefits?
Notes: To minimize the load of the root server.

## Slide 63: Three Enhancements on Look-up Algorithm
2. Recursion
  A client asks a name server "www.baidu.com"
  The name server does all the lookup through the tree and return the IP of Baidu to the client
  Usually, a name server has a better network connection

## Slide 64: DNS Request Process
Name client
Name client
ns.iss.edu
ginger.
Scholar.edu
NS: for edu
NS: for
Scholarly.edu
AP: for
ginger.Scholar.edu
ginger.
Scholar.edu
ginger.
Scholar.edu
names.edu
a.root.net
ns.iss.edu
names.edu
a.root.net
Recursion
Non-Recursion

## Slide 65: Three Enhancements on Look-up Algorithm
3. Caching
  DNS clients and name servers keep a cache of names
    Your browser will not do two look-ups for one address
  Cache has expire time limit
    Controlled by a time-to-live parameter in the response itself
    E.g., SJTU sets the TTL of www.sjtu.edu.cn to 24h
  TTL (Time To Live)
    Long TTL VS. short TTL
    Q: what are the tradeoffs?

## Slide 66: Combine These Enhancements
If:
  Many machines at SJTU use the SJTU name server for their initial DNS query
  The name server offers recursive querying and caching
Then:
  The name server's cache will hold many bindings
  Performance benefits from this large cache

## Slide 67: Other Features of DNS
At least two identical replica servers
  80 replicas of the root name server in 2008
  Replicas are placed separated around the world

## Slide 68: Other Features of DNS
Organization's name server (e.g., SJTU)
  Several replicas in campus
    To enable communications within the organization
  At least one out of the campus
    To validate the address for outside world

## Slide 69: Name Discovery in DNS (at the first place)
A client must discover the name of a nearby name server
  Name discovery broadcast to ISP at first time
  Ask network manager
  Ask by email, Google, etc.

## Slide 70: Comparing Hostname & Filename
They are both for more user friendly
  File-name -> inode number
  Host-name -> IP address
  The file-name and host-name are hierarchical; inode num and IP address are plane
They are both not a part of the object
  File-name is not a part of a file (stored in directory)
  Host-name is not a part of a website (stored on name server)
Name and value binding
  File: 1-name -> N-values (no); N-name -> 1-value (yes)
  DNS: 1-name -> N-values (yes); N-name -> 1-value (yes)

## Slide 71
Behind the DNS Design
Why was DNS designed in this way?

## Slide 72: Benefits of Hierarchical Design
Hierarchies delegate responsibility
Each zone is only responsible for a small portion
Hierarchies also limit interaction between modules
  A type of de-centralization

## Slide 73: Good Points on DNS Design
Global names (assuming same root servers)
  No need to specific a context
  DNS has no trouble generating unique names
  The name can also be user-friendly
Scalable in performance
  Simplicity: look-up is simple and can be done by a PC
  Caching: reduce number of total queries
  Delegation: many name severs handle lookups

## Slide 74: Good Points on DNS Design
Scalable in management
  Each zone makes its own policy decision on binding
  Hierarchy is great here
Fault tolerant
  If one name server breaks, other will still work
  Duplicated name server for a same zone

## Slide 75: Bad Points on DNS Design
Policy
  Who should control the root zone, .com zone, etc.? Governments?
Significant load on root servers
  Many DNS clients starts by talking to root server
  Many queries for non-existent names, becomes a DoS attack
Security
  How does a client know if the response is correct?
  How does VeriSign know "change Amazon.com IP" is legal?

## Slide 76: DNS Amplification Attack

## Slide 77: DNS Security
DNS Hijack: Cutting the binding between name and IP
DNS DoS (Denial of Service) attack
  BAOFENG.com & DNSPod
  2009-5-18: DNSPod was attacked and banned
  2009-5-19: The Internet in China was almost down
  Fixed timer: query for BAOFENG.com once per second!
Solutions
  /etc/hosts, dnsmasq, OpenDNS, etc.
  DNS shield to defend against DoS attack

## Slide 78: DNSSEC: Protect DNS Record
Only part of the zones are using DNSSEC, e.g., .gov, .org

## Slide 79
Naming Scheme
Naming: the glue of modules

## Slide 80: Naming in General
  ipads.se.sjtu.edu.cn – hostname
  steven@apple.com - email
  steven – username
  EAX - x86 processor register name
  main() - function name
  WebBrowser - class name
  /courses/cse/index.html - path name (fully-qualified)
  index.html - path name (relative)
  http://ipads.se.sjtu.edu.cn/courses/cse/index.html - URL
  13918275839- Phone number
  202.120.40.188 - IP Address

## Slide 81: Naming a Disk
File name: /dev/sda1
  As a special type of inode: device inode
  8,0 as (major, minor)
PCI address (name): 19:00.0
  SCSI storage controller: LSI Logic / Symbios Logic SAS1068E PCI-Express Fusion-MPT SAS (rev 08)

## Slide 82: Naming for Modularity
Retrieval: e.g., using URL to get a web page
Sharing: e.g., passing an object reference to a function
  Save space as well: only sending the name, not the object
Hiding: e.g., using a file name without knowing file system
  Can support access control: use an object only if knowing its name
  E.g., Windows has many undocumented API
User-friendly identifiers: e.g., “homework.txt” instead of 0x051DE540
Indirection: e.g., OS can move the location of the file data without notifying the user
  Have you ever defragmented your hard driver?

## Slide 83: Addresses as Names
Software uses these names in an obvious way
  E.g., memory addresses
Hardware modules connected to a bus
  Use bus addresses (a kind of name) for interconnection

## Slide 84: Naming Schemes
A naming schemes contains three parts:
  1. Set of all possible names
    You cannot use ‘for’ as a variable in C
  2. Set of all possible values
  3. Look-up algorithm to translate a name into a value
    or a set of values, or “none”

## Slide 85: Naming Model

## Slide 86: Naming Terminology
Binding – A mapping from a name to value
  Unbind is to delete the mapping
  A name that has a mapping is bound
A name mapping algorithm resolves a name

## Slide 87: Naming Context
Type-1: context and name are separated
  E.g., inode number’s context is the file system
Type-2: context is part of the name
  E.g., xiayubin@sjtu.edu.cn
Name spaces with only one possible context are called universal name spaces
  Example: credit card number, UUID, email address

## Slide 88: Determining Context - 1
Hard code it in the resolver
  Examples: Many universal name spaces work this way
Embedded in name itself
  cse@sjtu.edu.cn:
    Name = “cse”
    Context = “sjtu.edu.cn”
  /ipads.se.sjtu.edu.cn/courses/cse/README :
    Name = “README”
    Context = “/ipads.se.sjtu.edu.cn/courses/cse”

## Slide 89: Determining Context - 2
Taken from environment (Dynamic)
  Unix cmd: “rm foo”:
    Name = “foo”, context is current dir
    Question: how to find the binary of “rm” command?
  Read memory 0x7c911109:
    Name = “0x7c911109”,
    Context is thread’s address space
Many errors in systems due to using wrong context

## Slide 90: Name Mapping Algorithms - 1
Table lookup
  Find name in a table
    E.g., Phone book
  Context: which table?
    Implicit VS. explicit
    Default context

## Slide 91: Name Mapping Algorithms - 2
Recursive lookup
  E.g., “/usr/bin/rm”
  First find “usr” in “/”, then find “bin” in “/usr”, then “rm”
  Each look-up process is the same
Multiple lookup
  Recall: how to find “rm” without absolute name?
  $PATH
    E.g., “/usr/local/sbin:/usr/local/bin:/usr/sbin:/usr/bin:/sbin:/bin”
  Look-up in a predefined list of context

## Slide 92: Interpreter Naming API
value ← RESOLVE(name, context)
  Return the mapping of name in the context
status ← BIND(name, value, context)
  Establish a name to value mapping in the context
status ← UNBIND(name, context)
  Delete name from context
list ← ENUMERATE(context)
  Return a list of all bindings
result ← COMPARE(name1, name2)
  Check if name1 and name2 are equal

## Slide 93: FAQ of Naming Scheme - 1
What is the syntax of names?
What are the possible value?
What context is used to resolve names?
Who specifies the context?
Is a particular name global (context-free) or local?

## Slide 94: FAQ of Naming Scheme - 2
Does every name have a value?
  Or, can you have “dangling” names?
Can a single name have multiple values?
Does every value have a name?
  Or, can you name everything?
Can a single value have multiple names?
  Or, are there synonyms?
Can the value corresponding to a name change over time?